## Slide 1: NDN-DPDK: NDN Forwarding at 100 Gbps on Commodity Hardware
Junxiao Shi, Davide Pesavento, Lotfi Benmohamed
Advanced Network Technologies Division
National Institute of Standards and Technology

## Slide 2: Quick Recap from 2018-2019
NDN-DPDK is a high-speed NDN forwarder.
Goal: line speed on commodity hardware. How to get there?
Adopt better algorithms and data structures.
  2-stage LPM in FIB.
  PIT-CS Composite Table.
Reduce overhead in library and kernel.
  Multi-threaded architecture.
  Hugepage memory pools.

## Slide 3: New Features
input0
input1
Name Dispatch Table
output0
output1
input stage
forwarding stage
output stage
FIB replica
(one per NUMA socket)
crypto
helper
disk
service
fwd0
PIT+CS
fwd1
PIT+CS
NEW CoDel queues
RESTRUCTURED to better support forwarding hints
IMPROVED
packet decoder
reassembler
EXPANDED platform support

## Slide 4: AQM and Congestion Control
CoDel-like active queue management.
  Applied on ingress: bottleneck is in forwarding threads, not link bandwidth.
  Each packet type has a separate queue.
  Prioritize Data over Interest: dropping Data wastes resource spent on processing the Interest.
CUBIC-like congestion control in the traffic generator.
  React to congestion marks. Retransmit based on RTO.
forwarding thread
Interest queue
Data queue
Nack queue
input0
input1
output0
output1

## Slide 5: Benchmarks
Spoiler alert: we made it to 100 Gbps

## Slide 6: Benchmark Topology
Two physical machines:
Forwarder.
Traffic generators:
  Each instance operates independently.
  Fetch Data from each other.
CPU: dual Intel Xeon Gold 6240.
  18 cores at 2.60 GHz, Hyper Threading disabled.
Memory: 256 GB, 2933 MHz, four channels.
  64x 1GB hugepages per NUMA socket.
NIC: Mellanox ConnectX-5 100 Gbps.
forwarder
producer /A
consumer /B
producer /B
consumer /A

## Slide 7: We Made It to 100 Gbps
108 Gbps
Measured from consumers.
Data packets only.
Not counting retransmissions.
Data payload only.
8 forwarding threads.

## Slide 8: Input Thread Bottleneck
Expectation:
  # forwarding threads
  Data forwarding rate (pps)
Reality:
  Data forwarding rate plateaus at 8 forwarding threads.
Bottleneck: input thread.
  Current architecture only allows one input thread per face.
peak: 1.84 Mpps
linear growth
no improvement

## Slide 9: Effect of Nonlocal Memory Access
NUMA#0
gen
gen
NUMA#1
NUMA#0
gen
gen
NUMA#1
same NUMA
cross NUMA: higher memory access latency
up to 20% slower

## Slide 10: Hardware Acceleration
Removing the input thread bottleneck

## Slide 11: Inside an Input Thread
dispatch(interest, NDT[SipHash(prefix)].fwd);
dispatch(data, pitToken.fwd);
L2 decode
reassembly
L3 decode
Name Dispatch Table
dispatch by name prefix
dispatch by token
fwd0
fwd1
Interest
Data or Nack
network interface
input stage
Hardware dispatches most packets directly to fwd threads.
implement in hardware?

## Slide 12: Receive Side Scaling (RSS)
10/100G Ethernet adapter, receive path
ingress
Receive Side Scaling (RSS) rules
If field F has value V, dispatch to queue Q.
⁞
Otherwise, drop the packet.
queue 0
queue 1
queue 2
mempool
thread
mempool
thread
mempool
thread
NIC has ≥16 RX queues.
Configurable per queue:
thread to process packets
mempool to store packets into (ideally, on the same NUMA socket as the processing thread)
Choices of F are limited by hardware functionality:
ConnectX-5 only supports fields in Ethernet/IP/UDP/TCP headers.
Some cards allow "bytes at offset I" generic fields.
Incoming frames are matched against RSS rules and dispatched to queues.

## Slide 13: Input Dispatching with RSS?
L2 decode
reassembly
L3 decode
Name Dispatch Table
dispatch by name prefix
dispatch by token
fwd0
fwd1
Interest
Data or Nack
network interface
input stage
Infeasible with RSS, but not every packet needs reassembly.
Possible with RSS via "bytes at offset I" field.
Infeasible with RSS.
Name has variable length.

## Slide 14: Can NIC Understand Names?
"NDN-NIC: Name-based Filtering on Network Interface Card" (ICN'16)
  if (BloomFilter(XorHash(name))) { accept(pkt); } else { drop(pkt); }
  Python simulation.
NDN-DPDK Interest dispatching:
  dispatch(pkt, NDT[SipHash(prefix)].queue);
We need real hardware implementation.

## Slide 15: Collaboration Opportunities
Hardware implementation:
  eBPF
  P4
  FPGA
Algorithm modeling:
  Congestion control.
  Disk-based caching policies.
Real traffic trace for evaluation.
Application use case:
  Data intensive science
  Live video streaming
Library integration:
your library?
your app?

## Slide 16: NDN-DPDK Codebase
https://github.com/usnistgov/ndn-dpdk
  Forwarder
  Traffic Generator
  GraphQL-based management tools
  NDNgo library
Chart: Programming Languages (2020)
| qty
Go | 0.652
C | 0.297
TypeScript | 0.023
other | 0.028
Chart: Programming Languages (2019)
| qty
Go | 0.443
C | 0.494
TypeScript | 0.035
other | 0.028

## Slide 17: Expanded Platform Support
Operating systems:
  Ubuntu 18.04
  Debian 10
  CentOS 8
Virtualization and containers:
  VirtualBox
  Docker
  KVM
Ethernet adapters:
  Mellanox ConnectX-5
  Intel i350 and Intel X710
  other NICs via XDP driver
Network transports:
  Ethernet
  Ethernet with VLAN
  VXLAN tunnel (UDP)
Local application support:
  shared memory transport (memif)
  NDNgo application library
Experiment platforms:
  Run NDN-DPDK on a laptop (e.g. 4 cores, 8GB RAM)
  Deploy on the NDN testbed
  FABRIC testbed
new
regularly tested
known to work
planned

## Slide 18: NDN-DPDK on FABRIC Testbed
NDN-DPDK Experiment Profile
Launch a network of NDN-DPDK forwarders and traffic generators across multiple locations.
You can customize:
  Applications.
  Routing protocols and forwarding strategies.
  Caching algorithms.
Collect measurements.
  Packet timing and statistics.

## Slide 19: Q&A
Please attend NDN-DPDK presentation at ACM ICN 2020 conference.