## Slide 1: PLI-Sync: Prefetch Loss-Insensitive Sync for NDN Group Streaming
Yi Hu, Constantin Serban, Lan Wang, Alex Afanasyev, Lixia Zhang
This work was supported in part by DARPA under contract HR0011-17-C-0113. The views, opinions and/or findings expressed are those of the authors and should not be interpreted as representing the official views or policies of the Department of Defense or the U.S. Government. Distribution Statement "A" (Approved for Public Release, Distribution Unlimited.

## Slide 2: The Problem
Group multi-party stream data transfer
Dynamic content production
Stochastic data production interval
Goals:
Operate in reduced bandwidth environments: low overhead
Low latency
Disconnected Intermittent Links (DIL),lossy links, frequent/permanently partitioned networks
Producer
Consumer
2
1
3
4
5
Producer
Consumer
1
2
3
4
5
Producer
Consumer
3
1
2
4
5
Producer
Consumer
4
1
2
3
5
Producer
Consumer
5
1
2
3
4
1
2
3
4
5
Producer
Consumer

## Slide 3: Motivation
Conventional Sync approach:
Producer notifies consumers when data is available via separate sync protocol
  Immediate notification to satisfy latency constraints
Consumers obtain data name from sync protocol and fetch data
Issues: large overhead, per-data item sync and fetch overhead
Proposed approach:
Optimistic content pre-fetching: low latency and low overhead
State vector-based sync protocol: additional small and fixed overhead sync layer that provides operations in DIL conditions

## Slide 4: Approach
Optimistic Prefetching:
  Stream-oriented namespace: /data/Prod#/Stream#/Seq#
  Once consumer has received a piece of data, optimistically issues an interest for the next seq#
  Before sync notification and before data production
  Use heuristics/learning for setting Interest lifetime
Producer
Stream
Consumer
Streams
Producer
Consumer
PLI-Sync
NDN Library Layer
Application Logic /
Presentation
NFD
Interest
Data
Interest
Data
Interest
Sync Plane
Data Plane
NDN Network
PLI-Sync Streaming Node
State Vector Sync
  Periodic Interest-based notification of state vector from each node
  State: latest seq number for each producer/each stream
  Bootstrapping
  Lossy operations

## Slide 5: Approach – cont’ed
State Vector state updates
  At each producer
  At each data consumer
  At each sync consumer
Significantly increases the efficiency and throughput of the protocol and reduces its latency and overhead.
Producer
Consumer
Sync
PLI-Sync
Stack
A
B
C
A
B
C
A[10]
A[15]
A[15]
A[15]
A[15]
A[20]
t0
t1
Consumers fetch data eagerly
Local NFDs of consumer nodes cache data
PLI Sync hence enables data fetching in disconnected networks

## Slide 6: Results
Setup
50 nodes, 5 groups
Each node is a producer and a consumer
20% loss n->AP, 20% loss AP->n
No loss AP <-> LH
AP1
n1 ~ n10
AP2
n11 ~ n20
AP3
n21 ~ n30
AP4
n31 ~ n40
AP5
n41 ~ n50
LH
Metrics:
Overall Interest to Data Ratio (OIDR): total number of interests sent (data and sync planes)/data items received
Data Interest to Data Ratio (DIDR): number of data-plane interests / number of data items received
Sync Interest to Data Ratio (SIDR): number of sync interests sent / number of data items received
Efficiency (EFF): total bytes of received data at all end nodes / total sent bytes at all nodes
 | OIDR | DIDR | SIDR | Eff
PLI-sync | 1.88 | 1.87 | 0.06 | 13.4
PLI-sync-nocons | 2.66 | 2.08 | 0.58 | 3.0
PartialSync | 4.88 | 1.68 | 0.18 | 0.45

## Slide 7: Conclusions
New PLI-Sync targeting low-overhead low latency in DIL environments
Optimistic prefetch and periodic sync planes help each other for increased efficiency
Further considerations
  Congestion control
  Asymmetric group operations
  Differentiated reliability/latency services
  Predictability of data production rate
  …