## Slide 1: NDN in DARPA SHARE NDNCOMM, Sept. 2020
John DeHart
jdd@wustl.edu

## Slide 2: Statement and Disclaimer
Statement: This research was developed with funding from the Defense Advanced Research Projects Agency (DARPA).
Disclaimer: The views, opinions and/or findings expressed are those of the author and should not be interpreted as representing the official views or policies of the Department of Defense or the U.S. Government.

## Slide 3: Outline
Background
Team
Physical Architecture
NDN in DARPA SHARE
  Performance Studies
Conclusion

## Slide 4: Background
Open Network Lab (ONL) (https://onl.wustl.edu/)
  Internet-accessible network testbed built and hosted at Washington Univ. in St. Louis
  Rapid emulation of wide variety of network topologies and conditions.
  Capabilities to set network link loss, delay etc.
  Monitoring capabilities for immediate visual feedback.
  Data collection for post processing analysis.
DARPA seedling grant (2016) to look at NDN vs. IP in lossy and intermittent environments.
  Demonstrated on the Open Network Lab (ONL) at WUSTL, NDN sync with network intermediate component outperforming IP and VPN/IP in challenged intermittent environments.

## Slide 5: Background (continued)
DARPA SHARE (10/17 – present)
  Secure Handhelds on Assured Resilient networks at the tactical Edge
  Working on team led by Two Six Labs
  Secure Android handhelds using NDN operating in challenged network environments
  Program extended for fourth year to support technology transition
Challenged network environments:
  Low BW links
  Lossy and/or intermittent links
  Temporarily segmented networks
First two years focused on Android over wireless and cellular
Third and fourth years:
  Expanding to battlefield scenarios
  Android phones coupled to tactical radios
    How to provide more reliable data transport for tactical apps?

## Slide 6: Team
DARPA
  Joe Evans: PM for first two years
  Paul Zablocky: PM 10/2019 – 4/2020
  Mary Schurgot: PM 4/2020 – present
  And supporting cast
TwoSix Labs: Prime Contractor
  Eucleo
  Washington University
  Many other Subcontractors

## Slide 7: Physical Architecture
Phones
  Primary focus has been Android handheld devices
Topologies
  Initially focused on fixed infrastructure-based networks, such as WiFi and cellular
  Recently shifted to networking through tactical radios
  Even harsher BW limitations
MANET: Mobile Ad Hoc Networks
  Mesh networks with shifting connectivity as personnel move around

## Slide 8: NDN in DARPA SHARE
Version: 0.6.6
  Locked in during 2019
    Discussing how and when to update to current release
NDN Strengths and Weaknesses
  Weakness: Performance
  Strengths: Sync, Strategy layer, Security Model
Modifications
  Performance (client libraries and some NFD tweaks)
  ICT-Sync
  Local First Multicast (LFM) Strategy for Sync on MANET
  RandomCast-N Strategy for Data
  Persistent Interests for file transfer

## Slide 9: ICT-Sync
Multi-producer
Replaces digest with list of tuples in sync name
  Tuple: Participant id and latest sequence number published
  ICT-Sync name: /ndn/sync/syncId/[528:1][912:15][435:32]
Participant receiving sync interest:
  Compares its state to state in sync name
  Can immediately tell if there is a difference
  Can immediately tell what the difference is
  Responsible for requesting data in the associated data namespace
Future work to address scaling challenges related to name size

## Slide 10: Local First Multicast (LFM) Strategy
Using standard multicast in a mesh/MANET topology
  Sync interests contributed a lot of traffic
  How to make Sync more efficient?
Give local Sync process a chance to merge state before multicasting to all neighbor nodes
  Interest from remote face, if matched FIB entry
    Has a local face (Sync process), send there only
    Has no local face, multicast to all remote faces
  Interest from local face, multicast to all remote faces
Sync
Interest
Interest
NFD
Interest
Interest
Sync
Interest
Interest
NFD
✓
Sync
Interest
Interest
Interest
NFD
✕

## Slide 11: Performance Studies: LFM for Sync
Local First Multicast (LFM): Efficient routing strategy for bandwidth-limited networks
Test configuration: 25 nodes, fully connected mesh, 100 chunks, 20 secs (5 Hz)
Pulse width: Should be ~20 secs (receive all data in approx. how long it takes to publish it)
ONL real time monitoring charts show instantaneous link BW over time
SHARE NDN data strategy multicast
Standard NDN
Sync strategy:
multicast
Sync strategy:
LFM
Pulse: 438.4 sec
Pulse: 79.4 sec
Pulse: 33.2 sec
Pulse: 23.2 sec
8 Mb/s
8 Mb/s

## Slide 12: Performance Studies: Neighborhoods
Emulated evaluation of NDN performance of 25 nodes across a range of MANET topologies
  Focus on how various topologies benefit from or get stressed by NDN’s data synchronization
Experimentation details – conducted on emulated network in WUSTL’s Open Network Lab
  All 25 nodes publish data at 5 Hz (1000 chunks over 200 secs) and consume each other’s data
  Each link is rate-limited to 8Mbps (estimate for a particular tactical radio) with no loss and nominal delay of 5ms
  Each topology divided into “neighborhoods”, where all nodes in a neighborhood have next-hops to each other
  Instantaneous throughput monitored on select set of nodes (denoted by colored circles in figure below)
25-node
13-node
6-node
4-node
2-node
Full connected mesh
Daisy chain of nodes

## Slide 13: Performance Studies: Neighborhoods
Scenarios distribute data with 8 Mbps channels in allotted time (e.g. ~200 sec for 1000 chunks)
  Average network traffic loads decrease as the size of neighborhoods decrease
  Nodes that bridge between neighborhoods carry higher traffic loads
25-node neighborhood
8 Mb/s
13-node neighborhoods
6-node neighborhood
4-node neighborhood
2-node neighborhood
Throughput for 25 nodes in various topologies
Results indicate nodes may need to limit number of next-hop neighbors when fully connected
  For example: randomly pick a certain number of neighbors with which to create faces
  This led us to develop the randomcast-n# strategies

## Slide 14: RandomCast-N Strategy for Data
Nodes with M faces (where M is large)
  Multicast/broadcast overloads the network
For each Interest select N random faces out of M
  Multicast to those N faces
  Typical N’s we have found workable: 3 ≤ N ≤ 5
Relies on mesh being fairly well connected
  Randomization allows network to propagate interests to producers, even though NDN overlay is subset of underlying radio mesh

## Slide 15: Persistent Interests (PI)
Experimental: For severely BW limited operations.
Controversial: Breaks NDN flow balance principle
To reduce Interest overhead when retrieving large data items (Files, Maps, etc)
  CS returns all matching data
  Interest remains in PIT until it times out
  Interest continues to cause return of data if it arrives
  Producer responds with all of its matching data
After initial persistent interest times out, consumer:
  Sends new PI, with LAST_SEEN seq# indicator
  OR: Sends individual non-persistent interests for missing sequence numbers.

## Slide 16: Conclusion
DARPA SHARE has exercised NDN in new and challenging ways
We have shown NDN can perform successfully in these conditions
We plan to start feeding some of our code and modifications back into the NDN codebase
Still more work to do in the coming year…