## Slide 1: NDN Opportunities in 5G/6G Core Networks
Junxiao Shi, Davide Pesavento, Lotfi Benmohamed
Smart Connected Systems Division
National Institute of Standards and Technology

## Slide 2: In This Presentation
Very brief introduction of 5G core network
  Control-User Plane Separation
How to run NDN applications over 5G?
Simplify 5G/6G core architecture with NDN

## Slide 3: 5G Architecture
AMF
SMF
PCF
UDM
NEF
NRF
NSSF
AUSF
UPF
UPF
gNB
UE
DN
Radio Access Network (RAN)
Core Network – User Plane
packet routing and forwarding
traffic usage reporting
QoS handling
Core Network – Control Plane
authentication
mobility management
IP address allocation
…
Data Network (usually the Internet)
Core Network

## Slide 4: Run NDN Apps over 5G

## Slide 5: Use Case
Live video streaming from a 5G phone to worldwide viewers.
Carrier B
Carrier A
streamer
viewer
viewer
viewer
viewer
viewer
viewers on the same carrier
viewers on a different carrier
viewers on the Internet
Internet

## Slide 6: Baseline: NDN Routers on the Internet
Carrier B
Carrier A
Available today, but has drawbacks:
  The same Data packet flows through 5G core network multiple times.
  Limited QoS control, because 5G core network cannot see names.
streamer
viewer
viewer
viewer
viewer
viewer
NDN fw
NDN fw
UDP tunnels

## Slide 7: NDN Forwarding in 5G Core
IP UPF
NDN UPF
IP Internet
NDN Internet
control plane
gNB
NDN
UE
IP
UE
NDN AF
UE can connect to NDN, IP, or both data networks.
NDN Application Function
prefix registration
producer mobility support
centralized routing
NDN User Plane Function
stateful forwarding & caching
traffic usage reporting
QoS handling

## Slide 8: Enhanced: NDN UPF in 5G Core
Benefits:
  Interest aggregation and in-network caching available.
  Name-based QoS possible.
Carrier B
Carrier A
streamer
viewer
viewer
viewer
viewer
viewer
NDN fw
NDN fw
NDN UPF
NDN UPF

## Slide 9: Simplify 5G/6G Core Architecture with NDN

## Slide 10: Focus on the Control Plane
AMF
SMF
PCF
UDM
NEF
NRF
NSSF
AUSF
IP UPF
IP UPF
gNB
UE
IP
Radio Access Network (RAN)
Core Network – User Plane
Core Network – Control Plane
Data Network
NDN UPF
NDN

## Slide 11: Service Based Architecture
Control plane follows "micro-services approach":
  All control plane functions are connected to a "virtual bus" (IP subnet).
  Unified protocol stack: HTTP2/JSON.
Benefits: less complexity, better scalability.
AMF
SMF
PCF
UDM
NEF
NRF
NSSF
AUSF

## Slide 12: NF Repository Function (NRF)
NRF supports service discovery function.
  Every NF knows where is NRF.
  Every NF registers itself with the NRF.
  To talk to another NF, ask the NRF where it is.
AMF
NRF
AUSF
AUSF is at
192.168.11.25:8080
Where is AUSF?
AUSF is at
192.168.11.25:8080
HTTP request http://192.168.11.25:8080/<req>
HTTP response 200 OK

## Slide 13: Control Plane with NDN
It is still Service Based Architecture:
  All control plane functions are connected to a "virtual bus" (NDN LAN).
  Unified protocol stack: NDN/JSON.
NDN naming replaces service discovery.
Self-learning finds forwarding paths and helps with load balancing.
AMF
NRF
AUSF
Interest
/example-5g/ausf/<req>
Data /example-5g/ausf/<req>
OK

## Slide 14: Summary & Future Work
Two opportunities, in different layers:
NDN forwarder in 5G user plane enables stateful forwarding and in-network caching.
NDN can simplify 5G control plane, including service discovery and others.
These are just ideas…
  We need to think about protocol design and prototype implementation.
Certain commercial entities, equipment, or materials may be identified in this document in order to describe an experimental procedure or concept adequately. Such identification is not intended to imply recommendation or endorsement by the National Institute of Standards and Technology, nor is it intended to imply that the entities, materials, or equipment are necessarily the best available for the purpose.